## Slide 1
vRAN Cloud Native transistion
July, 2019

## Slide 2: Disclaimer
This presentation is proprietary information of Altiostar Networks, Inc. The information contained herein may not be used to create or change any contractual obligation of Altiostar Networks, Inc. Any review, retransmission, dissemination or other use of, or taking of any action in reliance upon this presentation by persons or entities other than the intended recipients is prohibited. This presentation is for planning and information purposes only. The specifications contained herein are subject to change without notice.
Any information contained in Altiostar’s product roadmap is intended to outline our general product direction. It is intended for information purposes only, and may not be incorporated into any contract. This does not constitute a promise or obligation of delivery of any product, feature, functionality or service and should not be relied upon in making purchasing decisions. Altiostar, at its sole discretion, and without notice, reserves the right to alter the design, specifications, and forecasted time to market of all of its products and services on any roadmap, at any time, as part of its continuing program of product development.

## Slide 3: Motivation to go to containers
Virtualization | vEMS | vCU | vDU | Comments
Horizontal Scaling | Not supported | Not supported | NA | Micro service architecture is highly recommended for reducing hardware resources and moving towards cloud native. DU is tightly coupled with RU. Horizontal scaling of DU like a web application is not that trivial.
High Availability | Yes | Not supported | No | Fault tolerance for vCU, vDU & EMS is only 99% (>5days/year). It should be atleast 99.9% (~8 hours/year). Desirable 99.99%(~5mins/year)
Resiliency | No | Only system level | No | Migrating to containers and adopting kubernetes can solve the issues of standalone machines
Automation | Cisco ESC | Cisco ESC | Cisco ESC | Onboarding CNF can be done by using helm charts and manifest.
Upgrade | 30 Mins | 15 mins for Upgrade | 20 mins | Zero down time can be achieved for upgrade if we adopt to container platform

## Slide 4: Challenges in vRAN for 5G w.r.t RT considerations
Processing budget at the BBU:
  In the LTE FDD setup, the Hybrid automatic repeat request (HARQ) mechanism with an 8 ms acknowledgment response time provides an upper bound for the total delay of both fronthaul latency and BBU processing time.
  The TTI (Transmit Time Interval) in LTE is 1ms. The packet scheduler gets invoked every ms. In 5G NR it is even more stringent. It can go upto 62.5 microsec (0.0625 ms). Current requirements are to support upto
Requirements of the RT-OS and Virtualization-System:
  To successfully provide frame/subframe timings, the execution environment of the DU has to support strict deadlines of the code execution.
  Load variations in the cell (e.g., day/night load shifts) impose the requirement on the on-demand resource provisioning and load balancing of the BBU pool.

## Slide 5: Requirements Latency, Jitter and Signal Processing
Fronthaul should still maintain the latency requirement to
meet the HARQ deadlines.
RTT between RRH and BBU equipped with a CPRI link cannot exceed 700 micro secs for LTE and > 400 µ secs for 5G.
Jitter required by advanced CoMP schemes in the MIMO case is below 65 ns as specified in 3GPP 36.104.
Next Generation Mobile Networks (NGMN) adopts the maximum front haul round-trip-time latency of 500 µ sec.
The propagation delay, corresponding to timing advance, between RRH and UE, affects only the UE processing time. The timing advance value can be up to 0.67 ms.
Consequently, this leaves the BBU PHY layer only with around 2.3–2.6 ms for signal processing at a centralized processing pool.
This is a general information. Not specifically impacting Virtualization or Containerization

## Slide 6: Container vs VM Performances in eNB (Ref 1.2)
I/O Performance Analysis & BBU processing time in Containers are extremely efficient with 4-5 times lower round trip times (RTT) as KVM has a high variations, and requires optimization to lower the Interrupt response delay as well as host OS scheduling delay.
Inter-arrival time of the packets collected from the eNBs served by the Application (SDN Controller). Increase in number of eNBs gradually resulted in significant difference in the behavior of the VM and Container test beds.
IPC latency increases exponentially in case of KVM and in containers platform it is as good as baremetal.
Inter-arrival time of the packets collected from the eNBs served by the Application (SDN Controller). Increase in number of eNBs gradually resulted in significant difference in the behavior of the VM and Container test beds.
Average waiting time from eNB to application and vice versa, for the VM and Container based architecture. Due to the fact the hardware resource of physical machine that is virtualized using VMs would easily get over-loaded with the increase in the number of virtual nodes.

## Slide 7: Business Line
5G from day 1 needs to be containerized. Starting with VM initially and then later moving to containers will never happen as it brings operational issues of moving all DU sites from VM to Containers without downtime.
      Rakuten wants to move away from CVIM / Redhat dependency
DevOps process will be very simplified with tools like Kubernetes
NetOps process will be very quick and we can adopt tools like ONAP in future

## Slide 8: Who are supporting Containers Platform?
Cloud Native Orchestrators | Preference | Advantage | Disadvantage
OpenNess | High | Wide range of options, provides Edge platform for Containers, Baremetal & VM. Moreover, stack is prepared for Telco world. | Only support OVS as their SDN
RiftWare | Moderate | More close to Telco stack. Automation & NetOps process can be simpler. Supports multiple SDN platform. | Do Not have a strong community
Openshift | Low | Community wise they are very strong. Web based application, they have good hands-on. Ready to work with us in-house to migrate our EMS to containers. | Fare away from Telco Stack. Understanding Telco protocols for transport and security interfaces is very low.

## Slide 9: Action plan
Action Plan:
Cloud Native training for Dockers & Kubernetes
Build EMS on microservices, with Innovation labs support.
Work with Intel Openness team and deploy vCU and vDU in edge

## Slide 10: References:
“vRAN - Increased agility with network flexibility | Mavenir”
https://mavenir.com/solutions/cost-reduction/virtualized-ran-vran
“Cloud Native Applications in a Telco World –OpenStack”
https://www.openstack.org/assets/presentation-media/5G-Cloud-Native-v4.pdf
“Why Do You Need a 5G Cloud-Native Core? | Light Reading”
https://www.lightreading.com/mobile/packet-core/why-do-you-need-a-5g-cloud-native-core/a/d-id/745195
“Towards a Cloud-Native Radio Access Network”
https://pdfs.semanticscholar.org/cfd6/14b9f7efec2deb2821c2cbfbb988a5ed7bb2.pdf
“Cloud-Native: What Does It Mean for Infrastructure?”
https://www.networkcomputing.com/networking/cloud-native-what-does-it-mean-infrastructure
“Achieving Cloud-Native HPC Capabilities in a Mixed Workload Environment”
https://thenewstack.io/achieving-cloud-native-hpc-capabilities-mixed-workload-environment/